## Slide 1: Use of Industry 4.0 for Predictive Asset Maintenance
Rick R. Durham Watson-IoT PMQ
Data Scientist
6/19/2017
The
ptiMA
Team:
Himanshu Mate
Kaustubh Meshram
Rajnandni Sharma
Surisetty Rohit
Vasu Chourasia

## Slide 2
2
J & J has been engaging extensively in delivering sutures and hence poses us to Identify and list the right set of hardware (equipment) as well as software requirements in order to implement Industry 4.0 to optimize the maintenance frequency without impacting MTBF/MTTR and machine health.
Adding on to the existing incorporations, it even encourages us to Develop a roadmap for implementing Industry 4.0 on manufacturing shop floor for implementing Predictive Maintenance of machines in Johnson & Johnson
Business Case Details:
Business Case Details
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
Insight 1
Insight 2
Insight 3
Edge in Action
Conclusion
Business Case Details
Our Aim

## Slide 3
Business Case Details
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
Implementation
Enablers
Future State
Impact
Recommendations
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
1
2
3
Edge in Action
Conclusion
Business Case Details
Predicting than Reacting
The basis of a predictive manufacturing system is the smart software, which is used to control predictive modeling functionalities where Databases help them do this by automating much of the analysis processes.
Predictive analytics helps manufacturing companies keep their machines running by comparing past machine failures to sensor data from the machines to recognize patterns before breakdowns happen
Three Key Challenges
Maintenance Architecture
Insight 1
Insight 2
Insight 3
Edge in Action
Conclusion
Business Case Details
Our Aim
Predicting than Reacting

## Slide 4
Three key challenges
Collect data from equipment
Create features
Build model and get actionable insights
Business Case Details
Three Key Challenges
Maintenance Architecture
Implementation
Enablers
Future State
Impact
Recommendations
Predicting than Reacting
Three Key Challenges
Predicting than Reacting
Maintenance Architecture
1
2
3
Edge in Action
Conclusion
Business Case Details
Three Key Challenges
Predicting than Reacting
Maintenance Architecture
Insight 1
Insight 2
Insight 3
Edge in Action
Conclusion
Business Case Details
Our Aim
Three Key Challenges

## Slide 5
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
Insight 1
Insight 2
Insight 3
Edge in Action
Conclusion
Business Case Details
Our Aim
Vibration Sensor
Pressure Sensor
Temperature
Sensor
Sensor Controller (SW)
l
Arduino
GSM Module
IoT Sensor Node
Cloud Storage
Raspberry Pi
Alert Message !!!
Remote Monitoring
WiFi or Ethernet
(MQTT Protocol)

## Slide 6
Predicting than Reacting
Three Key Challenges
Implementation
Enablers
Future State
Impact
Recommendations
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
1
2
3
Edge in Action
Conclusion
Business Case Details
Predicting than Reacting
1
2
3
Edge in Action
Conclusion
Business Case Details
Three Key Challenges
Maintenance Architecture
Predicting than Reacting
Three Key Challenges
Insight 1
Insight 2
Insight 3
Edge in Action
Conclusion
Business Case Details
Our Aim
Maintenance Architecture
Notes: Presenter
2017-10-26 15:22:59
--------------------------------------------
With this slide we take the statistical and analytical concepts explained on the previous slide and go into greater detail regarding the modeling algorithms. The various models are described below. One of the key points to be made in this slide is that PM’s sophisticated statistical and analytical models help an organization determine which of many sources of asset performance data are the most relevant in describing asset performance and predicting failure. In most cases by applying the statistical and analytical models we determine that ONLY A SUBSET of asset performance data is required to develop an accurate model. In one customer example, they began be identifying over 4,000 potential factors that could describe asset performance, via analysis to determine which data best correlated to describe asset performance, reduced the number of factors to about 30.
See IBM Predictive Maintenance and Quality Version 2.5.0 Solution Guide Chapter 8 for details on predictive models.
The Maintenance predictive model helps you optimize your Preventive Maintenance System. In the past, a scheduler would optimize a plant's Preventive Maintenance System (PMS) by carefully altering the days that were allotted for maintenance in the OEM's default schedule. The IBM Predictive Maintenance and Quality Maintenance predictive model helps you to optimize your maintenance schedule using predictive analysis. Often, in a new setup of PMQ sensors in the plant, even if sensor data has not gained optimal maturity for effective predictions, there may be enough data in the plant's maintenance system (Maximo/ SAP-PM etc.) to initiate a Predictive Maintenance regime. IBM PMQ's Maintenance Analytics can work on such maintenance work orders alone and does not depend on any sensor data. Therefore, the Maintenance model may help to expedite the ROI of any Predictive Analytics system before any useful sensor data is obtained.
The Sensor Health predictive model analyzes an asset's sensor readings to help determine the likelihood that the asset will fail. If the likelihood of failure is high, you can schedule an urgent inspection of the machine. The Sensor Health model continuously monitors the health of a machine or an asset and predicts potential machine faults in real time. The model uses historical sensor data profile values stored in the KPI tables and keeps a running status to determine the current health of an asset. The Sensor Health model can also be used to predict the future health of an asset.
The Top Failure Reason predictive model helps you identify the top failure predictors for a given asset in order of their importance. You can then further analyze the identified reasons or parameters to assist in a guided trail from cause or root cause analysis to its respective pattern discovery. This model is used to analyze and discover the top percentile and number of parameters which are influential in predicting a machine's failure (or optimal health) and their relative importance.
The Integrated predictive model produces a predicted health score and days to maintenance for each asset or process at a site. The health score is used to determine an asset's performance. The health score determines how likely an asset is to fail. This health score model can continuously monitor machine or asset health and predict potential machine faults in real time. It uses historical defect and maintenance data, along with results of the other Analytics models, to determine the integrated health score and forecasted days to maintenance of an asset. The integrated model can also be used to predict the future health of an asset.
The Feature-based predictive model produces a resource's predicted health score and optimal maintenance period, and recommends inspection or changes to maintenance schedules. It is an improvement to Sensor Analytics in Predictive Maintenance and Quality 2.0. Feature-Based Analytics analyzes historical failures and planned or unplanned (breakdowns) maintenance orders that are generated in IBM Maximo. It predicts a resource's health score and optimal maintenance period, and recommends inspection or changes to maintenance schedules.
Using the aforementioned models that IBM provides with PMQ, clients can also modify and extend these to develop custom models to meet the specific needs of their business.
Ensemble model combines senor, maintenance, custom and feature-based models into a single combined model. It allows customers to develop a model on an incremental basis. As they gain additional asset performance data they can continually improve model accuracy using ensemble modeling capability.
IBM also offers industry-specific asset models for rotational equipment, turbo pumps, high-value assets, safety, turbines, energy optimization, substation transformers, distribution transformers, poles (electrical transmission) and power cables. IBM will continue to develop additional industry- and asset-specific models.

## Slide 7
Predicting than Reacting
Three Key Challenges
Future State
Impact
Recommendations
Business Case Details
Maintenance Architecture
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
1
2
Edge in Action
Conclusion
Business Case Details
3
Replacing filter in air handling unit (AHU)
  Step 1: What is the preferred moment of replacement?
  Step 2: Which data is available that says something
  about the filter?
  Step 3: Which theoretical background has this data?
  Step 4: From the data, can a model be obtained
  that predicts filter behaviour?
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
Insight 2
Insight 3
Edge in Action
Conclusion
Business Case Details
Our Aim
Insight 1
Notes: http://www.sterilityequipments.com/ethylene_oxide_sterilizer.html

## Slide 8
Step 1: What is the preferred moment of replacement?
According manufacturer 10.920 hours of operations (+/- 65 weeks)
Preferred moment of replacement
Honeywell
LPT00700TBYNKBAA01
Sensor Used:

## Slide 9
Step 2: Which data is available that says something about the filter?
First period (26 weeks)
Second period
(23 week)

## Slide 10
Step 3: Which theoretical background has this data?
  At a constant debit and volume the pollution of a filter can be described according the law of Boucher’s
log(P/Pi) = -J*VL
Pi [Pa] = initial pressure when clean
J [-] = Boucher’s ratio of filter pore blocking VL [m3] = Volume of air passing
Variable to be predict
P(t) = c0 + c1.eJ.V.t
C0 [Pa] = initial pressure of the clean filter clean
C1 [-] = Constant to determine
J [-] = Boucher’s ratio of filter pore blocking
P [Pa] = pressure over filter on time x

## Slide 11
Step 4: Can a model be obtained from the data to predict filter behaviour?
  Through 2th order polynomial regression an average model is obtained over both data periods.
First period (blue line):
R-square = 90%
Second period (red line):
R-square = 85%
Average regression function (black line):
P(t) = Pi + 2e0,08t

## Slide 12
Conclusions
  Filter needs to be replaced around 250Pa.
  Current filter replacement at +/- 4.000 hours (80-90 Pa)
  Model predicts 250Pa is reached at +/- 8.900 hours of operation.
Recommendations
  Dataset contains P < 100Pa. Extending the dataset with P > 100 Pa gives
outcome in obtaining a more accurate model
  Current replacement cycle can be optimized from 2 times to 1 time per year
  Prediction gives outcome to increase flexibility in maintenance planning

## Slide 13
Predicting than Reacting
Three Key Challenges
Enablers
Future State
Impact
Recommendations
Business Case Details
Maintenance Architecture
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
1
3
Edge in Action
Conclusion
Business Case Details
2
Replacing Shock Absorbers to prevent air leakage in the chamber
Step 1 : How the data will be available?
Step 2 : Which data is available that says something about the health of the shock absorber?
Step 3 : From the data, How we can predict the air leakage
      More efficiently?
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
Insight 1
Insight 3
Edge in Action
Conclusion
Business Case Details
Our Aim
Insight 2
Notes: Due to non-optimal compressed air levels results in wear and leakages in the sterilizer. Thus, for detection of pressure fluctuations, compressed air metrics of a sterilizer, all possible locations of leakages and analyses for cushioning time against wear is of utmost importance for maintaining optimal compressed air levels.

## Slide 14
Sensors Details:
Together with AES fieldbus system, the SPM module detects in advance when critical limits will be reached
and provides users with key information for early intervention.
  Step 1: How the data will be available?​

## Slide 15
Step 2 : Which data is available that says something about the health of shock absorbers?
Maintenance monitor – determining wear
The shock absorber in this configuration had been replaced in regular routine intervals determined on the basis of past experience with the individual application – purely as a precautionary measure and not based on actual facts. The SPM now uses the cylinder sensor data to analyze the cushioning's timing characteristics. Because cushioning time decreases over the service life of the shock absorber, it provides direct proof of its state of wear. As soon as a critical value is reached, an error message can be output to exchange the shock absorber before it fails.

## Slide 16
Step 3: From the data, How we can predict the air leakage​ more efficiently?
Energy efficiency – detecting leakages
Energy efficiency is a key economic factor. The SPM gives a clear indication of where and how compressed air consumption changes – and allows users to determine the location of possible leakages. Predictive diagnostics is one of the main arguments for efficient use of the SPM.

## Slide 17
Predicting than Reacting
Three Key Challenges
Enablers
Future State
Impact
Recommendations
Business Case Details
Maintenance Architecture
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
2
3
Edge in Action
Conclusion
Business Case Details
1
Replacing bearing in the Recirculation Blower
Step 1 : How the data will be available?
Step 2 : Which data is available that says something at the bearing health?
Step 3 : From the data, can a model be obtained that
  predicts bearing vibration behavior?
Step 4 : How we can analyze and examine the data
coming from our model?
Build a model to predict when a bearing in the Recirculation Blower is likely to fail based upon data gather from sensors (accelerometers) mounted on the bearing supports.
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
Insight 1
Insight 2
Edge in Action
Conclusion
Business Case Details
Our Aim
Insight 3

## Slide 18
  Step 1: How the data will be available?​
2 Sensors (accelerometers) installed on each Bearing (x and y axis)
Data Details:
  The analysis period range
  Two sensors for each bearing (x, y axis)
  Data recorded for a 1 second window every 5 or 10 minutes
  Sampling Rate 20 KHz
Sensor Used:
VC MEMS sensors
Click to add text

## Slide 19
Step 2 : Which data is available that says something
about the bearing health?
Notes: Data Preparation & Visualization :
Analyze the input Time Series data- Exploratory Data Analysis (EDA)
Iterate through each time series file containing accelerometer measurements and calculate the top 5 highest “frequency spikes” for each file (1 second intervals).
This creates a file for each bearing with 2156 records (four files total) for the interval that is going to be store in the Cloud Storage
Determine when failure will occur

## Slide 20
Step 3: From the data, can a model be obtained that
  predicts bearing vibration behavior?
Modeling:
  Dataset built combined data from Sensor 1 (good data) and Sensor 4 (data with fault occurring) * Assumption is that these bearings are the same with the same engineering specifications and exhibiting the same levels of vibration at key frequencies
  A Logistic Regression model was fitted to the data

## Slide 21
Step 4: How we can analyze and examine the data coming from our model?
The model was evaluated on training and test set with the following results. It should be notes this was against a very small dataset. Result likely to vary with more data.

## Slide 22
Deployment:
• A scoring stream was created to score as set of bearing records against the logistic model that was created in the modeling phase. Note: The dataset records for this scoring stream were previously converted from time series to FFT format this is a fairly trivial undertaking. In a production setting this processing would be added to the scoring stream.
• This scoring model could be used in a variety of deployment environments including:
• Edge Devices
• Cloud Based SaaS application
• On Perm operational system

## Slide 23
Three Key Challenges
Insight 1
Insight 2
Insight 3
Connecting Everything
Conclusion
The first step for many organizations is simply to use devices to automate the collection and preprocessing of large amounts of data lead to next levels of sophistication in the areas of response, prediction, and autonomy.
Industrial companies use sensors and computing for predictive maintenance, worker safety and operational efficiency, detecting changes in performance to keep machinery humming and intercept problems before they cause failures in near real time.
Cross-pollination of information technology and Operation Technology cooperate to expertise leading to both innovation and greater efficiency.
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
1
2
3
Conclusion
Business Case Details
Edge in Action
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
Insight 1
Insight 2
Insight 3
Conclusion
Business Case Details
Our Aim
Edge in Action
Notes: Join the MEET

## Slide 24
Problem Statement
Predicting than reacting
Maintenance Architecture
Steam
Pneunatic
Vaccum
IO Linkage
Conclusion
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
1
2
3
Edge in Action
Business Case Details
Conclusion
Predicting than Reacting
Three Key Challenges
Maintenance Architecture
Insight 1
Insight 2
Insight 3
Edge in Action
Conclusion
Business Case Details
Our Aim

## Slide 25
Thank You! Questions?
Thank You! Questions?
We thank J & J for such an enriching and learning case study challenge strengthening our practical real life ground knowledge webbed with IO.